## Slide 1
SXWS255
Energy Web Server
User guide
RA00161CH
06/22-01

## Slide 3
1 Licence Agreements 6
2 System requirements 10
3 Catalogue numbers 12
4 Compatible devices 14
4.1 Measuring / metering devices 14
5 Languages available 18
6 Implementation 20
7 Use 22
  7.1 Access 22
  7.1.1 Access rights 22
  7.1.2 Login procedure 23
  7.1.3 Changing of the display language 24
  7.1.4 Logout procedure 24
  7.2 Data display pages 25
  7.2.1 My panel board 25
  7.2.2 Consumptions: data & diagram. 28
  8 FAQ 38

## Slide 5
Licence Agreements

## Slide 6
IMPORTANT:
Please read the terms and conditions of this license agreement carefully before using the software (as defined below).
This is a license agreement between you and BTicino SpA (BTicino) which is located in viale Borri 231, 21100 Varese, Italy.
By opening this package, breaking the seal, clicking the “I agree” or “yes” button or otherwise indicating assent electronically, or loading the software, you agree to the terms and conditions of this license agreement.
If you do not agree to these terms and conditions, make no further use of the software, and contact your vendor or BTicino customer service for information on how to obtain a refund of the money you paid for the software.
  1. DEFINITIONS
  “Software” means:
  (a) all of the contents of the files of the software (“Energy Management Software”) either with a Web server (“Energy Web Server”);
  (b) related explanatory written materials or files (“Documentation”), fonts and the packaging of the product;
  (c) upgrades, modified versions, updates, additions, and copies of the foregoing, provided to you by BTicino at any time (collectively, “Updates”).
  “Use” means to access, install, download, copy, or otherwise benefit from using the functionality of the Software.
  2. GENERAL USE OF THE SOFTWARE
  2.1 License
  This contract is a license Agreement.
  BTicino grants you a right not exclusive and not transferable to use the Software according to the conditions ant terms defined below.
  2.2 Rights and obligations
  You may:
  - use one copy of the Software on a single computer. If a greater number of copies and/or number of computers is specified within the Documentation or the applicable transaction documentation from the authorized distributor or reseller from which you obtained the Software, you may use the Software in accordance with such specifications;
  - make one copy of the Software for back-up or archival purposes, or copy the Software onto the hard disk of Your computer and retain the original for back-up or archival purposes;
  - use the Software on a network, provided that you have a licensed copy of the Software for each computer that can access the Software over that network;
  - permanently transfer all of your rights in the Software granted under this License Agreement to another person or entity, provided that you retain no copies of the Software and the transferee agrees to the terms of this License Agreement. Partial transfer of your rights under this License Agreement shall not be permitted. For example, if the applicable documentation grants you the right to use multiple copies of the Software, only a transfer of the rights to use all such copies of the Software would be valid;
1 Licence Agreements

## Slide 7
2.2 Rights and obligations (continued)
- use the Software in accordance with any additional permitted uses which may be set forth below.
You may not, nor may you permit any other person to:
- sublicense, rent or lease any portion of the Software;
- reverse engineer, decompile, disassemble, modify, translate, make any attempt to discover the source code of the Software or create derivative works from the Software;
- use the Software as part of a facility management, timesharing, service provider or service bureau arrangement;
- use the Software in any manner that is not permitted pursuant to this License Agreement.
3. COPYRIGHT
The Software is the property of BTicino or his licensers and is protected by law.
4. LIMITED WARRANTY
Warranty period for Products shall be 12 (twelve) months from delivery date.
BTicino guarantees the smooth running of this software only with the use of products BTicino. He cannot be held responsible in case of malfunction due to the use of products others than products BTicino.
5. LIMITATIONS OF LIABILITY
BTicino cannot be held liable for any damages of any kind, including without limitation any consequential, operating loss, data loss, malfunction of other softwares installed on your computer or any lost profits resulting of the impossibility to use the software, even if BTicino has been aware of the possibility of such damage.
6. TERMINATION
BTicino has the right to terminate this Agreement by rights immediately by a written notification if you fail to comply with any term of this Agreement and in particular with the provision of article 2.2.
Upon termination of the license, you accept to destroy all copies of the Software and his Documentation.
7. GOVERNING LAW
This Agreement will be governed by Italian Law.
In the event of issues relating to the construction, validity and/or execution of this agreement the Parties undertake to find an amicable settlement.
Failing such a settlement, the disputes shall be submitted to the exclusive jurisdiction of the Court of Milan.

## Slide 8
1 Licence Agreements

## Slide 9
System requirements

## Slide 10
Display possible on: (Device, Operating system, Web Browser)
iPhone:
5 and following, iOS 10 and following, Safari
2 System requirements

## Slide 11
Catalogue number

## Slide 12
3 Catalogue number
    SXWS255: “Energy Web Server 255”
  Management up to 255* devices
  Note: 32 for each Gateway max. 32 Modbus addresses or 32 pulse counters
    * Recommended value 128
    Software version 3.10.0

## Slide 13
Compatible devices
4.1 Measuring / metering devices 14

## Slide 14
4 Compatible devices
4.1 Measuring / metering devices
  Range NEMO
    Multifunction measuring units RS485 :
      Nemo D4-L, Cat.No MF6FT40026
      Nemo D4-L +, Cat.Nos MF6HT40003, MF6HT40006, MF6HT4000H
      Nemo D4-e, Cat.No MFD4E06
      Nemo D4-Le, Cat.Nos MFD4421, MFD4422, KRNEMOD4LE080, KRNEMOD4LE142, KRNEMOD4LE190
      Nemo D4-Dc, Cat.Nos MF6DC4200H, MF6DC42006, MF6DC4206H, MF6DC42066
      Nemo D4-EC, Cat.Nos MKD4R63DT, MKD4R125DT, MFD4ORFCDT1, MFD41ORFCDT, MFD42ORFCDT
      Nemo 72-Le, Cat.Nos MF72421, MF72422
      Nemo 96HD-e, Cat.No MF96E06
      Nemo 96HD-Le, Cat.Nos MF96411 + IF96001, MF96412 + IF96001, MF96411 + IF96012, MF96412 + IF96012, MF96421, MF96422, KRNEMOHDLE080, KRNEMOHDLE142, KRNEMOHDLE190
      Nemo 96HD, Cat.Nos MF96001 + IF96001, MF96002 + IF96001, MF96001 + IF96012, MF96002 + IF96012
      Nemo 96HD+, Cat.Nos MF96021 + IF96001, MF96022 + IF96001, MF96021 + IF96012, MF96022 + IF96012
      Nemo 96EA, Cat.Nos MFQ96021 + IF96001, MFQ96022 + IF96001
      Nemo 96-EC, Cat.Nos MK96R63DT, MK96R125DT, MF96ORFCDT1, MF961ORFCDT, MF962ORFCDT
  Range NEMO (continued)
    Multifunction measuring units pulse output (via the Pulse Concentrators Cat.Nos IF4C001* or SXMIMP* or pulse input of Energy counters Cat.Nos CE2DF3DTCL1*, CE4DF3DTCL1* and CE4TBDTCL1*):
      Nemo D4-L +, Cat.Nos MF6HTU0003, MF6HTU0006, MF6HTU000H
      Nemo D4-Le, Cat.Nos MFD4411, MFD4412
      Nemo 72-Le, Cat.Nos MF72411, MF72412
      Nemo 96HD-Le, Cat.Nos MF96411, MF96412

## Slide 15
  Range CONTO
    Energy counters RS485:
      Conto D1, Cat.No CE11165A4
      Conto D2, Cat.Nos CE20195A4, CE2DF3DTCL1
      Conto D2 MID, Cat.Nos CE2DMID11, CE2DF3DTMID
      Conto D4-Pd, Cat.Nos CE4DT06A4, CE4DF3DTCL1
      Conto D4-Pd MID, Cat.Nos CE4DMID31, CE4DF3DTMID
      Conto D4-Pt, Cat.Nos CE4DT14A4, CE4DT12A6, CE4DT14A4, CE4DT14A6, CE4TBDTCL1
      Conto D4-Pt MID, Cat.Nos CE4DMID01, CE4TBDTMID
      Conto D6-Pd, Cat.No CE6DT1256
      Conto D6-Pd MID, Cat.No CE6DMID56
  Range CONTO (continued)
    Energy counters pulse output (via the Pulse Concentrators Cat.Nos IF4C001* or SXMIMP* or pulse input of Energy counters Cat.Nos CE2DF3DTCL1*, CE4DF3DTCL1* and CE4TBDTCL1*):
      Conto D1, Cat.No CE11165A2
      Conto D1 MID, Cat.No CE1DMID12
      Conto D2, Cat.Nos CE20195A2, CE2DF30PCL1
      Conto D2 MID, Cat.Nos CE2DMID12, CE2DF30PMID
      Conto D4-Pd, Cat.Nos CE4DT06A2, CE4DT06A23F, CE4DF30PCL1
      Conto D4-Pd MID, Cat.No CE4DMID22, CE4DMID32, CE4DF30PMID
      Conto D4-Pt, Cat.Nos CE4DT12A2, CE4DT14A2, CE4TB0PCL1
      Conto D6-Pd, Cat.No CE6DT1252
      Conto D6-Pd MID, Cat.No CE6DMID52

## Slide 16
4 Compatible devices
  Range NEMO SX
    Multifunction measuring devices:
      Single-phase connection via Closed Rogowski coil(s) – Cat.Nos SX3M63 and SXMM63
      Three-phase connection via Closed Rogowski coil(s) – Cat.Nos SXMT63 and SXMT125
      Single-phase or Three-phase (configurable) connection with CT - Cat.No SXMMT5
      Three-phase connection via Open Flexible Rogowski coils - Cat.Nos SXMR02, SXMR04, SXMR06 and SXMR08
    State and Control modules:
      Multifunction State Module - Cat.No SXMC02
      Multifunction Control Module - Cat.No SXM0C1
      via Modbus/NEMO SX interface - Cat.No SXI485
  Gas counters
    Any device with pulse output via the Pulse Concentrators Cat.Nos IF4C001* or SXMIMP* or pulse input of Energy counters Cat.Nos CE2DF3DTCL1*, CE4DF3DTCL1* and CE4TBDTCL1*
  Water counters
    Any device with pulse output via the Pulse Concentrators Cat.Nos IF4C001* or SXMIMP* or pulse input of Energy counters Cat.Nos CE2DF3DTCL1*, CE4DF3DTCL1* and CE4TBDTCL1*
      * Note: Pulse Concentrator and Energy counters with pulse input must be properly programmed to be compatible with the type of counter (Refer to the technical documentation of each device)
  Range Power factor controller ALPTEC
    ALPTEC3.2 + ExtRS485
    ALPTEC5.2 + ExtRS485
    ALPTEC8.2 + ExtRS485
    ALPTEC8 + ExtRS485
  “Generic” Measurement/Counting Devices with Modbus RS485 output
  Any “other manufacturers” meter or counter with Modbus RS485 output, limited only to positive active energy

## Slide 17
Languages available

## Slide 18
5 Languages available
Languages:
  中国
  Deutsch
  English
  Español
  Français
  Français (Belgique)
  Ελληνικά
  Italiano
  Nederlands (Belgïe)
  Nederlands
  Polski
  Portuguese
  Русский

## Slide 19
Implementation

## Slide 20
6 Implementation
ATTENTION!
The procedures for configuring the Web Server (Web Server configuration) and the System (System configuration) are only possible by accessing the Web server by a computer. (refer to the “User manual“)
By working locally on Smart-phones are available only setting options and all display pages of consumptions or of charging stations management.

## Slide 21
Use
7.1 Access 22
7.2 Data display pages 25

## Slide 22
7 Use
      7.1 Access
The access to the Web Server’s data is protected by identification codes (PIN and PUK codes).
Three types of “default” users are configurated:
“administrator”
“installer”
“user”
The home page ("home") will be different depending on the type of user that access to the device.
7.1.1 Access rights
“administrator”
Access to the pages:
My panel board
Consumptions: data & diagram.
Default access PIN code:
99999 (5 characters)
Default access PUK code:
00000 9999 00000 (14 characters)
“installer”
Access to the pages:
My panel board
Consumptions: data & diagram.
Default access PIN code:
55555 (5 characters)
Default access PUK code:
00000 5555 00000 (14 characters)
“user”
Access to the pages:
Consumptions: data & diagram.
Default access PIN code:
11111 (5 characters)
Default access PUK code:
00000 1111 00000 (14 characters)

## Slide 23
7.1.2 Login procedure
Connect to the Web Server from your smart-phone by typing in the web browser the IP address set in the configuration procedure (refer to the “User manual” § 7.5)
Web Server’s login page appears
Type an access PIN code( ex. 99999 - default PIN) then press on “OK”.
Type the access PUK code 00000 9999 00000 (default PUK) then press on “OK”.
Web Server’s home page appears

## Slide 24
7.1.3 Changing of the display language
In the Web Server’s Home page, touch on the list box in the lower part of the page to choose the proper language.
Note: this operation doesn’t change the default language. To change the default language follow the procedure described in the User manual (§ 7.8.1)
7.1.4 Logout procedure
The Logout icon appears in the Web Server’s home page.
Touch the logout icon.
A confirmation page appears.
Touch “Logout” or “Lock” to
confirm the exit from the web
server.
Note:
Logout  closing the session;
reconnection with the PIN
code.
Lock  temporary disabling of
the application; reconnection
with the codes PIN+PUK.
7 Use

## Slide 25
      7.2 Data display pages
7.2.1 My panel board
“Devices” page allows to view the data measure by each device added by the users and to .
In the Web Server’s home page press on “My panel board”
A page with the Devices list’s appears.
This page shows the devices
added with their characteristics
and status icons.
Possibility to choose a device
per “Gateway”, “Panel board”
or “All devices”.
Description of the device selection button
Modbus Address (Modbus Address - Position for counters with pulse output or Modbus Address - Indication of the virtual device type for the Master/Slave function)
Name of the device
Symbols of the functions associated to the Device
  Measure State
  Command Link Functionality
This symbol appears only if the Device integrates the state function related to a protection device and shows the circuit-breaker state:
Open
Closed
Tripped
Device status
  On
  Off
  Communication error
  The procedure to switch ON/OFF a device is described in the “User Manual” (§ 7.12.1).
4
5
3
2
1

## Slide 26
7 Use
      In the Devices list’s page press on a Device button.
Details page of the selected
device appears. The page is divided into two
parts:
section is the area where is possible to select two pages:
Measure: display of the quantities measured by a device:
Electricity measuring device: Energy, Power, Voltages/Currents /Frequency, THD (if available on the Device) and Harmonics (if available on the Device)
Note: for “generic” measurement/counting devices and “Virtual” devices created with the Master/Slave function, only the table with the value of positive active energy is available.
Water Counters: Water consumptions
Gas Counters: Gas consumptions
State/Com.: page dedicate to NEMO SX devices; display of devices status, control buttons… for each NEMO SX device/group of devices
A
section shows the values measured by the selected device.
Touch the two arrows in the lower part of the page to view the different tables for the selected quantity (e.g. for Power: Active, Reactive and Apparent power).
B
B
A

## Slide 27
      For Power Factor Controllers of ALPTEC range, “My panel board” page is structured as follows:
In the Devices list’s page press on a Power factor controller button.
Details page of the selected
PFC appears.
The page is divided into two parts:
section is the area where is possible to select two pages:
Measure: display of parameters and electrical quantities measured by the Power Factor Controller:
Steps: State ( : not inserted, : inserted), Residual power (in % for APLTEC3.2/5.2/8.2 and in kvar for ALPTEC8), Number of insertions and Insertion time for each step;
Others quantities: Power, Power Factor, Voltages/Currents/ Temperature, THD and Harmonics
State/Com.: display of residual time to maintenance (for APLTEC3.2/5.2/ 8.2) and possibility to reset this time;
section shows the values measured by the selected power factor controller
A
A
B
B
Touch the two arrows in the lower part of the page to pass to the page containing indication of the Global state of Steps (OK or Default) and AUTO/MAN control button used to show the state of the power factor controller and to switch the device between two operating modes
Press on one of the buttons to view the other measured electrical quantities.
Use two arrows in the lower part of the page to display the different tables for the selected electrical quantity (e.g. for the Power: Active, Reactive and Apparent power and Power factor).

## Slide 28
7.2.2 Consumptions: data & diagram.
“Consumptions” page allows to view the global or detailed consumptions of the devices added by the users.
In the Web Server’s home page press on “Consumptions: data & diagram.”
Consumptions page appears.
Are available 5 ways of displaying data:
Grand Total - Electricity (Electrical Consumptions of the entire installation)
Grand Total - Overall (Overall Consumption of the installation)
Partials (Consumptions per Load and/or Measure group)
Compare (Comparison of the Global Consumptions between two Devices)
Details (Consumptions of a single Device)
For each page are available:
1. Histograms of the consumptions divided per:
Day (per hours)
Month (per days)
Year (per months)
2.Values in:
Wh (and multiples of Wh), dm3 (and multiples of dm3) of water, dm3 (and multiples of dm3) of gas and “Wh (and multiples of Wh) equivalent” of gas. Note: displayed values (resolution , decimal values, etc.) depend only on the quantities read by the measuring instruments.
EUR (or other configured currency)
3. Comparison between the actual and the previous value (ex. today/yesterday, etc.)
1
2
3
7 Use

## Slide 29
      Grand Total - Electricity
In the Consumptions menu page press on “Grand Total - Electricity”.
Visualization of Total Energy (Ea+) Consumptions on histograms.
Press “Day”, “Month” or “Year” to
view consumptions on a different
time period (Day (per hours) /
Month (per days) / Year (per months)).
Press “Data” to view the table with the values (in kWh and EUR) of global consumptions in different time periods.
Note: in this visualization, consumption data for “virtual” devices not excluded from Total are also taken into account.
      Grand Total - Overall
In the Consumptions menu page press on “Grand Total - Overall”.
Visualization of Overall Consump- tions of the system on tables and on a pie chart showing:
consumptions subdivided per type:
Electricity (blue area)
Gas (violet area)
Water (yellow area)
consumptions valued according to the measurement unit and the currency set
Press “Day”, “Month” or “Year” to
view consumptions on a different
time period (Day (per hours) /
Month (per days) / Year (per months)).
Note: in this visualization, consumption data for “virtual” devices not excluded from Total are also taken into account.
Histograms
divided per Load
The percentage shown in the pie chart is calculated based on the currency set

## Slide 30
      Compare
In the Consumptions menu page press on “Compare”.
Comparison page of Consump- tions between two Devices.
Note: Selecting two non homogeneous Measuring Devices (ex Electricity and Gas), comparison is evaluated only according to the currency (EUR or other currency) and not according to the measurement units. It is not possible to compare kWh of energy and “Equivalent kWh of gas.
Touch the two arrows in the lower part of the page to view the comparison histograms on a different time period (Day / Month / Year).
Selection of two devices to be compared
Selection of Total or Detailed comparison between the two selected devices
      Partials - Groups and Loads
In the Consumptions menu page press on “Partials -
Groups and Load type”.
Loads list’s page appears.
This page shows “pre-defined”
loads and loads added by the
users;
Possibility to choose a load
filtering the research per “Measure
Group”.
Pressing on a load button the partials consumptions page appears.
Press the drop-down menu to view histograms over a different time period (Day/Month/Year).
7 Use

## Slide 31
Details
In the Consumptions menu page press on “Details”.
Devices list’s page appears.
This page shows the devices
added by the users with their
characteristics and status icons.
Possibility to choose a device
per “Group”, “Load” or
“All devices”.
Description of the device selection button
Modbus Address (Modbus Address - Position for counters with pulse output or Modbus Address - Indication of the virtual device type for the Master/Slave function)
Name of the device
Symbols of the functions associated to the Device
  Measure State
  Command Link Functionality
This symbol appears only if the Device integrates the state function related to a protection device and shows the circuit-breaker state:
Open
Closed
Tripped
Device status
  On
  Off
  Communication error
  The procedure to switch ON/OFF a device is described in the “User Manual” (§ 7.12.1).
4
5
3
2
1

## Slide 32
Press the drop-down menu to view energy histograms over a different time period (Day/ Month/Year).
Press on one of the buttons to view the other measured electrical quantities.
Use two arrows in the lower part of the page to display the different tables for the selected electrical quantity (e.g. for the Power: Active, Reactive and Apparent power and Power factor).
In the Devices list’s page press on a Device button.
Details page of the selected
device appears. The page is divided into two
parts:
section is the area where is possible to select two pages:
Measure: display of the quantities measured by a device:
Electricity measuring device: Energy, Power, Voltages/Currents /Frequency, THD (if available on the Device) and Harmonics (if available on the Device)
Note: for “generic” measurement/counting devices and “Virtual” devices created with the Master/Slave function, only Energy histograms are available.
Water Counters: Water consumptions
Gas Counters: Gas consumptions
State/Com.: page dedicate to NEMO SX devices; display of devices status for each NEMO SX device/group of devices
section shows histograms of the consumptions, values measured by the selected device, status icons (if available).
A
B
A
B
7 Use
Notes: 32

## Slide 33
      For Power Factor Controllers of ALPTEC range, “Details” page of the “Consumptions: data & diagram.” menu is structured as follows:
In the Devices list’s page press on a Power factor controller button.
Details page of the selected
PFC appears.
The page is divided into two parts:
section is the area where is possible to select two pages:
Measure: display of parameters and electrical quantities measured by the Power Factor Controller:
Power Fact: linear graphs with power factor trend
Others quantities: Power, Power Factor, Voltages/Currents/ Temperature, THD and Harmonics
section shows the values measured by the selected power factor controller
A
B
A
B
Press on one of the buttons to view the other measured electrical quantities.
Use two arrows in the lower part of the page to display the different tables for the selected electrical quantity (e.g. for the Power: Active, Reactive and Apparent power and Power factor).

## Slide 34
- Detailed view and direct download of data
Pressing on the button , it is possible to browse the histograms in detailed mode by : - Day (per hours) - Month (per days) - Year (per months) -10 years (per years)
Press the drop-down menu to select the histogram viewing period (Day, Month, Year, 10 years).
      Advanced histograms display
For consumptions histograms of the menus “Partial – Groups and Load types” and “Details”, an advanced display mode is available.
- Full screen display
Pressing on the button , histograms can be enlarged to full screen on the device.
Note: image format and resolution will depend on the screen on which the data will be displayed (see example for a 4,5” screen).
To return to the standard format, press the button at the top right.
7 Use

## Slide 35
Pressing on the three points “…“, another set of options is displayed.
Pressing on two arrows ( or ), it is possible to pass from one to another histogram in the selected period (e.g. today, yesterday, two days ago, ...).
Pressing on the button , it is possible to download a “.csv” file named “datalogger.csv” with the data saved by the web server in the selected period.
Pressing on the button , it is possible to return to the standard view.
Note: it is still possible to put in full screen this type of histogram by pressing the button .
Example: display by “Day” and choice of a specific date in the selected period.

## Slide 36
7 Use

## Slide 37
FAQ

## Slide 38
8 FAQ
ATTENTION!
Downloading and management of files .CSV and all other functions (management of the database, network types, terms of access and Backup/Restore procedure) are possible only by accessing the Web server by a computer (refer to the “User manual“)
Notes: 38

## Slide 40
IME reserves at any time the right to modify the contents of this booklet and to communicate in any
form and modality, the changes brought to the same.
BTicino SpA
Viale Borri, 231
2110 Varese – Italy
www.imeitaly.com